## Slide 1: TDM - PCM System (In Proteus)
Group 13
1706149
1706150
1706152
1706189

## Slide 2
3 channel input
Multiplexer
Analog To Digital Converter
Transmission channel
Demultiplexer
Decoder
Low Pass Filter
Parallel to Serial Data converter
Serial to Parallel Data converter
3 channel output
TDM - PCM System Block Diagram

## Slide 3: Main Circuit
Replace with your own text
Transmitter Side
Receiver Side
Multiplexer
ADC
PISO
SIPO
DAC
Demultiplexer
LPF
Transmission
channel

## Slide 4
Input is three sinusoidal signals of three different frequency
Amplitude: Peak to Peak 10 voltage

## Slide 5
CD4051 Multiplexer
Take input signal from 3 channels
Time division multiplexing occurred and generate data through a single channel
Output is Connected directly with ADC
Multiplexer

## Slide 6
Output Of TDM block

## Slide 7
ADC
ADC0804 IC is used
Sampling, Quantization and Encoding happened here
Voltage range 0-10v is used.
Clock frequency 4k Hz.
Generate code word data stream in DB0 ~ DB7
Connected to parallel to serial converter block

## Slide 8
Corresponding Decimal output for input signal formula

## Slide 9
Parallel to Serial Converter
74165 IC is used here, a Parallel to serial 8 bit shift register
It takes parallel input, deliver serial data
32k Hz clock frequency is used
Output of this block is used for transmission

## Slide 10
Output of parallel to serial converter

## Slide 11
Serial To Parallel Converter
74HC595 IC is used for serial to parallel converter
This block receives the data from the input DS.
Convert Serial line code into parallel data by 8 bit frame
Feeds parallel data bits through Decoder

## Slide 12
Serial To Parallel Converter
Decoder and Op Amp
DAC0808 decodes the data from each code word
Generate specific analog output level according to incoming code word
Output signal is inverted polarity and negatively biased

## Slide 13
Op amp is used as current to voltage converter , working as transimpedance amplifier
DAC changes the digital input into current , Op amp converts this current to voltage.

## Slide 14
Output Of decoder and Op Amp

## Slide 15
Time Division Demultiplexer
CD4051 demultiplexer
Complementary function of multiplexing
Extracts 3 channel outputs from incoming decoded signal
Same shape output is obtained , but high frequency components are present

## Slide 16
Two stage low Pass Filter
Low pass filter is used to make the three output signals smooth
Output is slightly attenuated compare to input signal. So, by amplifying we can solve this issue.

## Slide 17
Output and Input Comparison
Input signal 3
output signal 2
input signal 2
Output signal 3
Output signal 1
Input signal 1

## Slide 18
Contributions
1706149 : Decoding ,Demultiplexer , filtering, slide making
1706150 : parallel to serial and serial to parallel , decoding
1706152 : Idea and resource management ,report
1706189: multiplexing and encoding, report, slide

## Slide 19
Thank
You